## Slide 1: 樹莓派簡介
唯客學院

## Slide 2: RPi是什麼?

## Slide 4: 安裝Raspberry Pi Imager

## Slide 10: 怎麼安裝作業系統?

## Slide 11: 燒錄作業系統至RPi
使用 Raspberry Pi Imager (https://www.raspberrypi.org/software/)
Notes: https://www.raspberrypi.org/software/)

## Slide 20: 沒有螢幕、鍵盤？ 怎麼設定連線?

## Slide 21: Raspberry Pi Headless Connection
設定 wpa_supplicant.conf
Enable ssh (在boot建立一個 ssh 空白檔)
ctrl_interface=DIR=/var/run/wpa_supplicant GROUP=netdev
update_config=1
country=<Insert 2 letter ISO 3166-1 country code here>
network={
ssid="<Name of your wireless LAN>"
psk="<Password for your wireless LAN>"
}
wpa_supplicant.conf 範例：
Notes: https://www.raspberrypi.org/documentation/configuration/wireless/headless.md

## Slide 25: 怎麼連上RPi?

## Slide 26: 連線RPi
使用 ssh 連線 RPi (預設域名: raspberrypi.local)
  使用 putty 或作業系統內建的 ssh
  譬如: ssh pi@raspberrypi.local
  username: pi
  password: raspberry

## Slide 30: 什麼是MQTT?

## Slide 31
+
MQTT (Publish)
MQTT (Subscribe)
MQTT Broker

## Slide 32: 先在筆電上玩玩MQTT? 等一下再到RPi玩一次！

## Slide 33: 測試MQTT
Notes: https://www.hivemq.com/mqtt-client-library-encyclopedia/

## Slide 34: 遠端開發?

## Slide 35: Raspberry Pi Remote Development
“Remote SSH needs a Raspberry Pi 3 or 4. It is not supported on older Raspberry Pis, or on Raspberry Pi Zero.”
Notes: https://www.raspberrypi.org/blog/coding-on-raspberry-pi-remotely-with-visual-studio-code/

## Slide 57: 插個感測器？ 量量溫度跟濕度?

## Slide 58: 讀取DHT11溫濕度感測器
安裝必要套件：
pip3 install adafruit-circuitpython-dht
sudo apt-get install libgpiod2
Notes: https://learn.adafruit.com/dht-humidity-sensing-on-raspberry-pi-with-gdocs-logging/python-setup

## Slide 61: 讓程式開機後自動執行?

## Slide 62: 設定程式在RPi開機後自動執行
mkdir /home/pi/.config/autostart
編輯 .desktop 檔，放入 autostart 目錄中
chmod +x myscript.desktop
sudo reboot
[Desktop Entry]
Type=Application
Name=DHT11
Exec=/usr/bin/python3 /home/pi/code/dht11_mqtt.py
.desktop 檔 範例：
Notes: https://learn.sparkfun.com/tutorials/how-to-run-a-raspberry-pi-program-on-startup/introduction
https://www.raspberrypi.org/forums/viewtopic.php?t=294014

## Slide 63
Q & A
Notes: https://unsplash.com/photos/KdeqA3aTnBY

## Slide 64
THANK YOU
Notes: https://unsplash.com/photos/ruQHpukrN7c